## Slide 1: Wheel & Tire Tech Session
September 12, 2020
10:00 AM CDT
Presented by Houston MG Car Club

## Slide 2: History
Original tires were leather or steel
John Boyd Dunlop of Ireland produced the first production pneumatic tire

## Slide 3: Tire Treads
Slicks – No grooves, provides maximum contact area for higher traction
Mud & Snow (M&S) – Larger deeper slots to engage mud and snow(All season radial)
Snow – Deep tires some have studs to grip in ice but can damage road surface
Chains -

## Slide 4: Wear
  Tires an wear due to several factors:
    Poor alignment wearing inner and outer ribs
    Rocky terrain
    Under inflation causing wear to outer ribs
    Unbalanced wheels causing uneven wear
  Tread wear indicators show minimum tread
  Damage by aging
    Thermo oxidation degradation caused by time, temperature, flex fatigue, UV exposure

## Slide 5: Traction Grades

## Slide 6: Temperature Grades

## Slide 7: Date Code
Tires should not be more than 10 years old.

## Slide 8: Load Indexes
The higher the tire's load index number, the greater its load carrying capacity
Examples:
  89 = 1,279 pounds 88 = 1,235 pounds 87 = 1,201 pounds 86 = 1,168 pounds 85 = 1,135 pounds

## Slide 9: Speed Rating

## Slide 10: EuropeanTire Noise Rating
The external noise generated by the tire is indicated both in decibels (dBs) and by black sound waves that indicate the noise class of the tire, from 1 (quiet) to 3 (loud)
• 1 black sound wave: Already 3dB below the 2016 European limit • 2 black sound waves: Already com­pliant with the 2016 European limit • 3 black sound waves: Compliant with the 2012 European limit

## Slide 11: Tire Tread Material
The most common elastomer material used today is a styrene-butadienecopolymer. It combines the properties of polybutadiene, which is a highly rubbery polymer and thus offering good wet grip properties, with the properties of polystyrene, which is a glassy polymer and thus offering low rolling resistance in addition to wear resistance.
Therefore, the ratio the two monomers in the styrene-butadiene copolymer is considered key in determining its grip and wear resistance properties.

## Slide 12: Tubeless vs Tube-Type
Tubeless tires are considered safer because they do not loose air suddenly when punctured
Tubeless tires stay cooler as there is less friction
Tubeless tires are easier to balance as there is less uneven weight
Tires with tubes are better suited to wire wheels due to sealing around the spokes

## Slide 13: Wheels
Alloy wheel
Wire wheel
Steel wheel

## Slide 14: Tire Balancing
Static balancing
Dynamic Balancing

## Slide 15: Lug Centric vs Hub Centric
Hub Centric Wheels are centered by the center bore of the wheel and the hub flange.
Lug centric wheels are centered by the torque of the lug bolts; rather than the center bore of the wheel and the hub flange

## Slide 16: Wheel Adapters
Can be used to located lug centric wheels on balancing machine
Can be use to increase track width

## Slide 17: Trailer Tires
Usually stay in sunlight and do not move
This leads to premature wear
Typically 4 year life

## Slide 18: Thank You
Our sincere thanks to Mr Miles Sandy of Discount Tire.